Pre-Construction Meeting

Date:

Project Name:

#### Attendees

Name			Company		              Contact Information

______________	__________________            ___________________________

______________	__________________	 ___________________________

______________	__________________	 ___________________________

______________	__________________	 ___________________________

______________	__________________	 ___________________________

Letters of Credit/s:

- Erosion Control:

- Digging Permit:

- Subdivision:

Utility Testing:

- Sewer Pipe: Air Pressure Test and a Deflection Test (Mandrel)

- Sewer Manholes: Leakage Test (Vacuum)

- Water Pipe: Water Pressure Test and a Bacteria Test

- All PVC Pipes: Deflection Test (Mandrel)

CO Requirements: Letter of Credit, base pavement on road and sidewalk, and curbing.

Inspection Hours: Owner will be billed for the hours that the Engineering Department spends on the project.  This will include on-site inspections, plan review, phone calls and anything else related to the project.

The rate is $00.00 hourly      Initials (          )

General Information:

- All water pipe must be Polywrapped.

- All hydrants must be plugged (non-draining).

- The Engineering Department must witness all tests.

- A sketch must be provided if there are major changes to the approved plan.

- Shop drawings to be provided if necessary.

- Underdrains and filter fabric if necessary.

As Built Drawings: Must be on reproducible mylar and digital disk and must tie into the Dover GIS.

Emergency Numbers:

City Contacts: Engineering:	Dave White, Alan Dews (603) 516-6450                     Public Works: John Storer, Bill Boulanger, Joe Boucher (603) 516-6450

# Utilities: Brian Alonzi (603) 516-6459

## Police Dept Dispatch:  (603)-742-4646

## Cell: Alan Dews – 603-396-3962